## Slide 1: Characterizing CUDA and OpenMP Synchronization Primitives
Brandon Alexander Burtchell and Martin Burtscher
Department of Computer Science

## Slide 2: Motivation
Parallelism is now one of the primary methods of speeding up programs
When writing parallel code, it is often necessary to use synchronization primitives for correctness
Performance depends on many complex factors
  Non-trivial for beginners and experts alike
Hence, we need to identify the behavior of sync primitives to guide programmers

## Slide 3: Highlights
Create a test framework to measure throughput of single calls of synchronization primitives
Run experiments across several parameters
Analyze behavior and provide recommendations
This talk covers the most notable findings
Code and results are open-source
  github.com/burtscher/SyncPerformance

## Slide 4: Approach
To time a sync, we define two functions
  Baseline and Test
Identical functions, except the test executes the sync at least one more time than the baseline
Subtract the runtimes to yield the runtime of the sync—without testing overhead
Convert to throughput for analysis

## Slide 5: Approach: Test Template
Warmup removes overhead from fetching data from slower memory for the first time
Sync threads before starting per-thread timers
(Not shown) convert to throughput

## Slide 6: Approach: CUDA Template
Like OpenMP template, except it is a CUDA kernel
clock64() counts elapsed clock cycles

## Slide 7: Background: Covered Syncs
OpenMP barrier
  All threads must reach barrier before continuing
OpenMP atomic update (add)
  Read, update, and write to a memory location in a single uninterruptable atomic transaction (prevents data race)
OpenMP flush
CUDA atomicAdd()
CUDA warp shuffles
Full paper covers more

## Slide 8: Evaluation Methodology
Tested 3 systems
  Results shown from System 3
Parameters
  Number of threads
  Number of blocks (CUDA)
    1, 2, half, full, double capacity
  Type (int, ull, float, double)
  Stride of array accesses
9 runs per baseline/test

## Slide 9: Results

## Slide 10: OpenMP Results: Barrier
Dotted line is where hyperthreading starts
Relatively stable beyond 8 threads
Throughput of OpenMP barrier

## Slide 11: OpenMP Results: Atomic Add (Scalar)
Throughput of OpenMP atomic update on a single shared variable
Arithmetic (integer vs. floating-point) is the differentiator

## Slide 12: OpenMP Results: Atomic Add (Array)
Throughput of OpenMP atomic update on private elements in a shared array for different strides
Stride = 1
Stride = 4
Stride = 8
Stride = 16
Increasing stride reduces effect of false sharing
8-byte types are now padded to separate cache lines
Note: L1 cache line size is 64 bytes
Now no more false sharing

## Slide 13: Background: OpenMP Memory Flush
Memory consistency model specifies allowed reorderings of reads and writes of one variable relative to another
A memory flush prevents reorderings by ensuring all memory operations prior to the flush finish before any start that appear after the flush
  Necessary when programmer uses a variable to protect another (e.g., flag in producer-consumer code)

## Slide 14: OpenMP Results: Memory Flush
Throughput of OpenMP flush for different strides
Stride = 1
Stride = 4
Stride = 8
Stride = 16
8-byte types oscillate more (false sharing)
8-bytes types no longer have false sharing
Note: L1 cache line size is 64 bytes
Results from System 2

## Slide 15: OpenMP Recommendations
Barriers are not a major concern with large thread counts
Using hyperthreads does not significantly impact synchronization performance
Atomic updates/writes to the same memory location should be avoided
Atomic operations to different memory locations are faster if the locations do not reside in the same cache line

## Slide 16: CUDA Results: Atomic Add (Scalar)
Throughput of atomicAdd() on 1 shared variable
2 Blocks
64 Blocks
half # SMs
Warp-aggregated atomic!
Warp-aggregated atomic!
Slower float: fewer atomic units?
GPUs have 32-bit arch
Note: log scale on x-axis

## Slide 17: CUDA Results: Atomic Add (Array)
Throughput of atomicAdd() on private elements in a shared array for different block counts and strides
1 Block, Stride = 1
1 Block, Stride = 32
128 Blocks, Stride = 1
128 Blocks, Stride = 32
Stride has no effect on 1 block
More blocks, more traffic to shared L2 cache
Downward trends due to max number of atomics per time unit

## Slide 18: Background: CUDA Warp Shuffles
Warp shuffles synchronize the threads in a warp and have them exchange values
  __shfl_sync(), and up, down, xor variants
Example of using warp shuffles to perform a sum reduction
Image source: Lin, Y and Grover, V. “Using CUDA Warp-Level Primitives.”
https://developer.nvidia.com/blog/using-cuda-warp-level-primitives/

## Slide 19: CUDA Results: Shfl Sync
Throughput of __shfl_sync()
128 Blocks (“full”)
256 Blocks (“double”)
Throughput is constant to a point
64-bit types drop at half number of threads

## Slide 20: CUDA Recommendations
int atomic operations generally perform better than other data types
  Automatic warp-aggregated atomics are powerful
Other atomics (i.e., CAS, Exch) followed similar behavior, implying a hardware limit on the number of concurrent atomic operations
Warp shuffles are fast but decrease throughput when the SM is nearly fully loaded
  Still, they should be used to avoid memory traffic

## Slide 21: Conclusions
We hope this information aids developers
In the full paper, we cover much more
  OpenMP critical section, memory flush
  CUDA syncs, thread fences, warp-level functions
Future developers can write new tests
Acknowledgements: DOE, NVIDIA
Code and results are open-source
  github.com/burtscher/SyncPerformance
Contact: burtchell@txstate.edu